## Slide 1: Input/Output Modeling of Simple Artificial Cell Using Modularized Approach
Miroslav Gasparek, Imperial College London
Mentor: Richard Murray, Caltech
Co-mentor: Vipul Singhal
26 September 2017

## Slide 2: Introduction & Background
Miroslav Gasparek
Coming from Puchov, Slovakia
Year Two Undergraduate, Department of Bioengineering, Imperial College London
Interested in dynamical and control systems
I play accordion for more than 13 years

## Slide 3: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 4: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 5: Properties of living cells
Self-organization
Homeostasis
Reproduction
Growth
Metabolism
Adaptation to surrounding environment
Response to environmental stimuli
Reproduction
Sensing/
Membrane Import
Intracellular
Signaling
Regulation/Computation
Membrane Export
Output signal
Input signal
Alberts, B. (2014). Essential cell biology. New York: Garland Science.

## Slide 6: Properties of artificial cells
Self-organization
Homeostasis
Reproduction
Growth
Metabolism
Adaptation to surrounding environment
Response to environmental stimuli
Reproduction
Sensing/
Membrane Import
Intracellular
Signaling
Regulation/Computation
Membrane Export
Output signal
Input signal
Alberts, B. (2014). Essential cell biology. New York: Garland Science.

## Slide 7: Modular “bottom-up” approach
Biomolecular circuits as subsystems
Various subsystems
- Sensing
- Transport
- Signaling
- Regulatory
- Metabolic
“Building blocks” of artificial cell
Sensing/
Membrane Import
Intracellular
Signaling
Regulation/Computation
Membrane Export
Output signal
Input signal
Alberts, B. (2014). Essential cell biology. New York: Garland Science.

## Slide 8: Input/Output analysis
Current tools:
- in vitro cell-free approach (TX-TL)
- in silico MATLAB SimBiology TX-TL modeling toolbox
Issues:
Inability to model modular behavior in TX-TL
No way to connect subsystems
Need for simple modeling tool
for I/O modeling
Sensing/
Membrane Import
Intracellular
Signaling
Regulation/Computation
Membrane Export
Output signal
Input signal
RNAP, Enzymes…
Del Vecchio, D. and Murray, R. (2015). Biomolecular feedback systems. Princeton, NJ [u.a.]: Princeton Univ. Press.

## Slide 9: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 10: Modeling of interconnection of simple cellular subsystems
Diffusion into the cell
Double Phosphorylation Pathway
Incoherent
Feed-Forward Loop
Diffusion out of the cell
Output signal
Input signal

## Slide 11: BioSIMI
BioSIMI (“Biomolecular Subsystems Interconnection Modeling Instrument”)
Tool for simple I/O modeling of interconnected biomolecular subsystems
Multiple Input/Single Output modeling
User-defined (mainly transport) and TX-TL-defined (standard assembly)
Accounts for retroactivity and resource competition

## Slide 12: BioSIMI (I/O Model of Vesicle)
% Create SimBiology model object vesicle vesicle = BioSIMI_make_vesicle('vesicle') % Create subsystem with reactions and species in DiffusionIn subsystem DiffIn = BioSIMI_make_subsystem('DiffusionIn','input','output','DiffIn') % Add reactions and species in DiffusionIn subystem to the appropriate % compartments of vesicle object BioSIMI_add_subsystem(vesicle,{'int','ext'},DiffIn) % Create subsystem with reactions and species in Double-Phosphorylation subsystem DP_Subsystem = BioSIMI_make_subsystem('DP','in','out','DP_Subsystem') % Add reactions and species in Double-Phosphorylation subystem to the appropriate % compartments of vesicle object BioSIMI_add_subsystem(vesicle,'int',DP_Subsystem) % Connect DiffusionIn subsystem with Double-Phosphorylation subsystem and % create object of class subsystem that contains connection of both % subsystems DiffDP = BioSIMI_connect(vesicle,'int',DiffIn,DP_Subsystem,'DiffDP') % Create subsystem with reactions and species in IFFL subsystem IFFL_Subsystem = BioSIMI_make_subsystem('IFFL','in','out','IFFL_Subsystem') % Add reactions and species in IFFL subystem to the appropriate % compartments of vesicle object BioSIMI_add_subsystem(vesicle,'int',IFFL_Subsystem) % Connect the combination of DiffusionIn and Double-Phoshporylation subsystem with IFFL % subsystem and create object of class subsystem that contains connection % of all three subsystems Diff_DP_IFFL = BioSIMI_connect(vesicle,'int',DiffDP,IFFL_Subsystem,'Diff_DP_IFFL') % Create subsystem with reactions and species in DiffusionOut subsystem DiffOut = BioSIMI_make_subsystem('DiffusionOut','input','output','DiffOut') % Add reactions and species in DiffusionOut subystem to the appropriate % compartments of vesicle object BioSIMI_add_subsystem(vesicle,{'int','ext'},DiffOut) % Connect the combination of DiffusionIn, Double-Phoshporylation, and IFFL % subsystem with Diffusion Out subsystem and create object of class subsystem % that contains connection of all four subsystems subsystems FinalSystem = BioSIMI_connect(vesicle,'int',Diff_DP_IFFL,DiffOut,'FinalSystem') % Run the simulation of the Final System SimData = BioSIMI_runsim(FinalSystem,20) % Plot the Input/Output relationship in the Final System BioSIMI_plot(FinalSystem,SimData)

## Slide 13: BioSIMI (Multiple input/Single Output)

## Slide 14: BioSIMI (Multiple input/Single Output)
% Create SimBiology model object vesicle vesicle = BioSIMI_make_vesicle('vesicle'); % Create subsystem with reactions, parameters and species in the first Double-Phosphorylation subsystem DP_Subsystem1 = BioSIMI_make_subsystem('DP','in','out','DP_Subsystem1'); % Create subsystem with reactions, parameters and species in the second Double-Phosphorylation subsystem DP_Subsystem2 = BioSIMI_make_subsystem('DP','in','out','DP_Subsystem2'); % Create subsystem with reactions, parameters and species in Incoherent Feed-Forward Loop subsystem % Choose species activator protein A ('pA') and repressor protein B ('pB') % as inputs of IFFL subsystem IFFL_Subsystem = BioSIMI_make_subsystem('IFFL',{'pA','pB'},'out','IFFL_Subsystem'); % Add all subsystems into vesicle's internal compartment BioSIMI_add_subsystem(vesicle,'int',DP_Subsystem1); BioSIMI_add_subsystem(vesicle,'int',DP_Subsystem2); BioSIMI_add_subsystem(vesicle,'int',IFFL_Subsystem); % Create final system that consists of input subsystems and output % subsystem FinalSystem = BioSIMI_connect(vesicle,'int',{DP_Subsystem1,DP_Subsystem2},IFFL_Subsystem,'FinalSystem'); % Run the simulation of the Final System SimData = BioSIMI_runsim(FinalSystem); % Plot the Input/Output relationship in the Final System BioSIMI_plot(FinalSystem,SimData);

## Slide 15: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 16: Connecting TX-TL systems
Incoherent Feed-Forward Loop + Gene Expression TX-TL reaction
Incoherent
Feed-Forward Loop
Gene Expression Reaction
Arabinose
Protein deGFP*
Amino acids, AGTP…
Protein deGFP-lva*
RNAP

## Slide 17: BioSIMI (I/O modeling of multiple TX-TL subsystems)
%% Create Incoherent Feed-Forward Loop (IFFL) circuit in TX-TL modeling toolbox % Set up the standard TXTL tubes tube1 = txtl_extract('E30VNPRL'); tube2 = txtl_buffer('E30VNPRL'); tube3 = txtl_newtube('circuit_closed_loop_withClpX'); % Define the DNA strands (defines TX-TL species + reactions) txtl_add_dna(tube3, 'p70(50)', 'utr1(20)', 'AraC(600)',0.5*4.5, 'plasmid'); txtl_add_dna(tube3, 'pBAD(50)', 'utr1(20)', 'tetR(600)', 2*4.5, 'plasmid'); txtl_add_dna(tube3,'pBAD_ptet(150)', 'utr1(20)', 'deGFP(1000)-lva(20)',4*4.5, 'plasmid'); txtl_add_dna(tube3,'p70(50)', 'utr1(20)', 'ClpX(600)',0.1*4.5, 'plasmid'); % Add species to the tube 3 txtl_addspecies(tube3, 'arabinose', 10000); txtl_addspecies(tube3, 'aTc', 1000); ClpXToAdd = 80; % ClpX are added % Mix the contents of the individual tubes % Create Model Object 'IFFL' that can serve as model object for 'IFFL subsystem' IFFL = txtl_combine([tube1, tube2, tube3]); %% Create subsystem for 'IFFL' circuit assembled in TX-TL above IFFL_Subsystem = BioSIMI_make_subsystem(IFFL,'arabinose','protein deGFP-lva*','IFFL_Subsystem'); | %% Create simple Gene Expression (GenExp) circuit in TX-TL modeling toolbox % Set up the standard TXTL tubes tube1 = txtl_extract('E30VNPRL'); tube2 = txtl_buffer('E30VNPRL'); tube3 = txtl_newtube('gene_expression'); % Define the DNA strands (defines TX-TL species + reactions) dna_deGFP = txtl_add_dna(tube3, ... 'p70(50)', 'utr1(20)', 'deGFP(1000)', ... % promoter, rbs, gene 30, ... % concentration (nM) 'plasmid'); % type % Mix the contents of the individual tubes % Create Model Object 'GenExp' that can serve as model object for 'GenExp subsystem' GenExp = txtl_combine([tube1, tube2, tube3]); %% Create subsystem for 'GenExp' circuit assembled in TX-TL above GenExp_Subsystem = BioSIMI_make_subsystem(GenExp,'RNAP','protein deGFP*','GenExp_Subsystem'); %% Create new subsystem 'FinalSystem' that contains species from connected 'IFFL' and 'GenExp' subsystems FinalSystem = BioSIMI_connect_txtl('FinalSystem','int',IFFL_Subsystem,GenExp_Subsystem,'FinalSystem'); % Create new subsystem 'FS' that removes repeated species and the unused output of 'input subsystem' % Set up events, parameters, and reactions in the final subsystem 'FS' FS = BioSIMI_assemble(FinalSystem,'FS'); % Simulate final subsystem 'FS' with assembled reactions for (14*60*60) seconds SimData = BioSIMI_runsim(FS,14*60*60); % Plot time dependences of input (arabinose) and output (protein deGFP*) of interconnection of IFFL and GenExp subsystems BioSIMI_plot(FS,SimData);

## Slide 18: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 19: Input/output characteristics of liposome-encapsulated toggle switch
Interconnection of user-defined
and TX-TL-created subsystems:
  IPTG initially present (“OFF”)
  Import of aTc through diffusion
  Sequestration of TetR
  Increased yield of GFP (“ON”)
  GFP export by channel-mediated diffusion
LacI
GFP
TetR
pTet
pLac
Input 1: IPTG
Input 2: aTc

## Slide 20: Input/output characteristics of the liposome-encapsulated toggle switch
Variation in time of addition of the aTc
Variation in diffusion rate of the aTc

## Slide 21: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 22: Encapsulation of TX-TL in lipid vesicles
Liposome vesicles prepared using protocol by Jonsson, Noireaux, Adamala and all
Attempt to encapsulate protein GFP and Luciferase
Luciferase Failed, GFP successfully encapsulated
Vesicle with encapsulated GFP

## Slide 23: Optimization of protocol for liposome preparation
Variations in experimental protocol were applied:
- Decrease in centrifuging speed (20 000g to 5000g)
- Change in method of the lipid vesicle extraction (bottom vs. top)
- Number of washes by buffer (1 wash vs. 3 washes)
Extraction from the bottom + multiple washing = no vesicles observed
For extraction from the bottom, single wash is optimal

## Slide 24: Contents
Motivation & Background
Modeling of interconnection of simple cellular subsystems in BioSIMI
Interconnection of TX-TL reactions using BioSIMI
Input/output characteristics of genetic toggle switch encapsulated in the liposome
Summary of experimental work
Conclusion and the future plans

## Slide 25: Conclusion
Development of BioSIMI framework for modeling I/O behavior of subsystems interconnection:
- Creation of several user-defined subsystems (transport, signaling, regulatory)
- Compatibility with TX-TL modeling toolbox
- Multiple input/Single Output
- Rapid, user-friendly modeling
- Demonstration of several use-cases (multiple subsystems, TX-TL, toggle switch)
Experimental investigation of liposome formation
- Contribution to optimization of the experimental protocol
- Further work required for robust process

## Slide 26: Further plans
Use of parameter identification to optimize I/O characteristics
Modeling of the sensor-reporter system with genetic toggle switch (orthogonal communication, concentration sensor)
Experimental investigation of the sensor-reporter system
Finalization of BioSIMI development (Multiple Inputs-Multiple Outputs)
Simulation of large population of vesicles
Response to stochasticity in the input

## Slide 27: Acknowledgements
Professor Richard Murray – big picture insights and challenging suggestions!
Vipul Singhal – great hands-on and hands-off mentoring and keeping me up!
Shaobin Guo – patience in the lab and answers to all my questions!
Miki Yun – teaching me PCR, TX-TL, proper pipetting and other crucial life skills!
… And thanks to all the members of the Murray Lab